The motor MB 837 BA -500 is a standalone liquid chilled 8 cylinder diesel with mechanical supercharging.

The motor works in four-stroke pre-process.

Technical data:

Type						BA 837-Ba 500

Maker						MTU

Design						V-Form 90 degree

Fuel						Diesel

Performance					four-stroke pre-process with mechanical supercharging

Number of cylinders				8

Total capacity					29.900 cm3

Rated power					460 - 483 KW , according to DIN 2200/min

Maximum  torque				2206 NM at 1750/min

Rated power					11 KW/t

Idle speed					600-630 ( motor operating )

Injection sequence				1-8-4-2-7-3-6-5

Empty charge highest speed			2400 - 2460 / min

Full charge highest speed				2200 / min  ( rated speed  )

Maximum admissable operating speed		2350 / min

Lowest operating speed				1500 / min

Cooling						Water circulation cooling

Coolant						115 Litre

Direction of rotation 				Left ( regard flywheel )

Mass						1550 kilo

Maximum length with clutch			1360 mm

Maximum width					1060 mm

Maximum height					1096 mm